## Slide 1
Energy from the Sun Workshop
Introduction to Solar Energy

## Slide 2: Review: Atomic Structure
Three particles
Nucleus
Electrostatic Force
Strong nuclear force
Notes: The atom is made of three particles: Protons, which are positively charged; Neutrons, which have no electrical charge (neutral); and Electrons, which are negatively charged. The neutron is the largest particle, being ever so slightly more massive than the proton. However, for practical intents and purposes, the neutron and proton have the same mass, especially when compared to the infinitesimally tiny, virtually massless, electron.
The nucleus is the location of the protons and neutrons. It is the place where the mass of the atom is concentrated, and has an overall positive charge.
Moving around the nucleus are the electrons, in mathematically calculated pathways called orbitals. Note two things about this diagram: First, it is not drawn to scale (most of the volume of the atom is empty space between the nucleus and the electron cloud); and Second, the electrons do not move nearly as predictably or neatly around the nucleus as shown.
The electrons are moving at nearly the speed of light. They are bound to the atom because of the electrostatic attraction between them and the protons in the nucleus. Their momentum keeps them from crashing into the center of the atom.
The nucleus stays together in spite of the electrostatic repulsion between the protons. This is because of a fundamental force, called strong nuclear force, that is associated with neutrons. It keeps the nucleus together. The energy required to hold a nucleus together is called binding energy. Iron nuclei are most stable, and have the lowest amount of binding energy per particle in the nucleus (nucleon). Therefore, iron can neither be fused nor fissioned.

## Slide 3: Radiant Energy
Notes: Under extreme pressure, and at extremely high temperatures, nuclei of atoms and their electrons can separate, forming something called plasma. In this extremely high energy state, nuclei can get close enough to each other to fuse. When they fuse, they release tremendous amounts of energy. This is what happens in the sun’s core.
The energy produced by fusion can be reabsorbed by other nuclei and re-released in subsequent fusion reactions. Generally, energy released in the core of the sun can take thousands of year to find its way to the surface of the sun.
Once the energy has left the sun, it is radiated as electromagnetic radiation toward space at a speed of 300 million meters per second, or 186,000 miles per second. At that speed, the energy needs only 8 minutes to reach the outer atmosphere of the earth 93 million miles away.
Once it reaches the earth, the incoming solar radiation, or insolation, is absorbed and reflected as shown. The greenhouse effect, a naturally-occurring phenomenon, allows the energy from the sun to remain trapped near the earth’s surface, keeping the temperature of the earth in a comfortable range at night. Without the greenhouse effect, life on earth would be impossible.

## Slide 4: Variances in Solar Radiation
Notes: The amount of insolation that reaches the earth is consistently the same amount. However, any given location on the earth’s surface will receive varying amounts due to the tilt, rotation and revolution of the earth, as well as cloud cover and particulate matter in the atmosphere. The time of day, season, latitude, and daily weather patterns all affect the amount of available solar energy in a particular location.

## Slide 5: Average Daily Solar Insolation Per Month
Notes: Due to these four factors, the average number of peak sun hours per day varies from one area of the country to another.
Solar insolation is the solar radiation incident on an area over time.
Solar insolation is equivalent to solar energy and is usually expressed in kilowatts-hours per square meter

## Slide 6: Major Uses of Solar Energy
Daylight
Drying Agricultural Products
Space Heating
Heating Water
Generating Electrical Power
  Concentrating Solar Power
  Photovoltaics

## Slide 7: Daylighting
Notes: Using skylights, tube lights, and large windows on the sunward side of a building help maximize the amount of light reaching the interior of a building and reduce the need for artificial lights.

## Slide 8: Daylighting
Notes: Langston High School in Arlington, VA and Caywood Elementary in Kentucky use daylighting to keep energy costs down.

## Slide 9: Drying Agricultural Products
Notes: Crops such as wheat and rice have been allowed to dry in the fields for centuries. Hay is mown and allowed to dry in the field before being baled. A small solar collector is used to dry herbs. Agricultural products can be dried in a special tower that uses a solar collector to heat air and channel it through perforated trays of crops, which dries them and carries the moisture out through the top.

## Slide 10: Space Heating Through Passive Solar
Notes: Passive solar design involves using specific shapes, angles, and building materials to maximize the amount of solar energy allowed into the interior of a building during cold months. Overhangs are used to shield the home from the high, summer sun, but are designed to allow the low, winter sunlight to enter the windows.
Materials, such as concrete and stone, are used to absorb the sun’s energy and store it, releasing it into the home at night after the sun has set. This is called direct gain.
Other features, such as sunspaces and trombe walls, can be used. A sunspace uses glass in a fashion similar to the way a greenhouse does. The heated air within the sunspace is then allowed to circulate throughout the building. A trombe wall is made of a specific absorbing material, and is often painted black or covered with glass (or both) to maximize the amount of energy absorbed and keep it locked inside. The thermal energy is then released to the building slowly over time, providing warmth throughout the night.

## Slide 11: Passive Solar
Notes: These homes in Montana and California with a passive solar design heats the home in the winter and cools the home in the winter.

## Slide 12: Active Solar Heating
Notes: Active solar heating is much like passive solar heating except it takes the power of the sun and amplifies it.
The people living in this house enjoy heated water using a solar thermal system.
Flat plate solar collectors are usually large flat boxes with one or more glass covers. Inside the boxes are dark colored metal plates that absorb heat. Air or liquid, such as water, flows through the tubes and is warmed by heat stored in the plates. These systems are particularly useful for providing hot water to households.

## Slide 13: Solar Collector
Glass on outside
Absorbent on inside
Circulating Fluid

## Slide 14: Generating Electrical Power
Concentrating Solar Power
  Trough systems
  Power towers
Heat exchanger plus steam turbine
Photovoltaics
  Small-scale (buildings) kW production
  Large-scale (utilities) MW production
Photoelectric effect

## Slide 15: Concentrating Solar Power
Notes: A clean, large-scale solar thermal technology known as concentrating solar power is used in special power plants (Concentrating Solar Power or CSP plants) that use different kinds of mirror configurations to convert the sun's energy into high-temperature heat. The heat energy is then used to generate electricity in a steam generator.

## Slide 16: Power Tower
Notes: World’s largest solar power tower in Seville, Spain.
Solar power tower consists of a large field of sun tracking mirrors, called heliostats, which focus solar energy on a receiver atop of a centrally located tower. The enormous amount of energy, coming out of the suns rays, concentrated at one point (the tower in the middle) produces temperatures of approx. 550 C TO 1500 C.
The gained thermal energy can be used for heating water or molten salt, which saves the energy for later use. Heated water gets to steam, which is used to move the turbine generator. This way thermal energy is converted into electricity.

## Slide 17: How a Power Tower Works
Notes: This graphic shows how the power tower is used to heat molten salt which is used to heat water to produce steam to turn a turbine which produces electricity.
Molten salt is used to transfer the heat because the heat can be stored and used when the sun is behind the clouds or at night.

## Slide 18: Photovoltaics
Notes: Exelon City Solar in Chicago, IL – this tracking flat-panel installation has 32,292 panels rated at a total of 10 MW capacity (DC).

## Slide 19: Solar Utility Installations in California

## Slide 20: Demand Response (www.caiso.com)

## Slide 21: Load Balancing and the Grid

## Slide 22: For More Information
If you have questions, we have answers:
www.need.org – our website
info@need.org – questions about NEED
cturrel@need.org – questions about this workshop
1-800-875-5029 – NEED main office phone number